MATERIAL SAFETY DATA SHEET

# SECTION I	IDENTIFICATION

Emergency Phone Number	CHEMTREC - 1-800-424-9300

Chemical Family	Organic salt solution

Chemical Name & Synonyms:	N/A – Mixture

Formula:	Proprietary

Trade Name & Synonym:	GOLDEN HARVEST PLUS  5-18-2 GA

SARA/TITLE III HAZARD CATEGORIES (See Section X)

Immediate (ACUTE) Health:	NO                             Reactive Hazard:    NO

Delayed (Chronic) Health:	NO                             Sudden Release of Pressure:  NO

Fire Hazard:	NO

# SECTION II	PRODUCT AND COMPONENT HAZARD DATA

APPROX.

A.	COMPONENTS	CAS. REG. NO	        %     	       TLV

Phosphoric Acid	   7664-38-2                        7.5%              1.0 mg/m3 Vapor/8 hrs.

Zinc Sulphate                               7733-02-0                        6.0%                 None established

Manganese Sulphate                    7785-87-7                        7.0%                 5 mg/m3 (As Mn)

Ferrous Sulphate                          7782.63.0                         7.0%                1 mg/m3 (As Fe)

# SECTION III	PHYSICAL DATA

Appearance and Odour:	Thick brown liquid, sweet odour

Boiling Point:	212( F. (approx.)

Specific Gravity:	1.46

Vapor Pressure:	Not established

Percent Volatile by Volume:	Proprietary

Vapor Density (Air = 1)	<1.0

Evaporation Rate:	(Ethyl Ether = 1): <Water

Solubility in Water:	>99%

.

# SECTION IV	FIRE AND EXPLOSION HAZARD DATA

Flash Point:	N/A

Flammable Limits:	N/A

Extinguishing Agent:	Water, CO2 or Dry Chemicals

Special Fire Fighting Procedures:	Wear self-contained breathing apparatus

Unusual Fire and Explosion Hazards:	Toxic fumes may be generated at elevated temperatures.

PAGE 1 OF 3

- ANIMAL TOXICITY DATA

Manganese Sulphate Eye (rbt)= moderate

# SECTION V	REACTIVITY DATA

Stability:	Stable

Incompatibility

Hazardous Decomposition Products:	Oxides of sulphur, nitrogen, and phosphorous

Products:

Hazardous Polymerization:	None

SECTION VI	TOXICITY AND HEALTH

- EXPOSURE LIMITS

OSHA Permissible Exposure Limit (PEL):	Not determines

Threshold Limit Value (TLV):		1 mg/m3 Vapor/8 hrs. for Phosphoric Acid,

1 mg/m3 for Ferrous Sulphate

- EFFECTS OF OVEREXPOSURE

- ACUTE

a.	Inhalation:	Irritation to nasal and respiratory passages

b.	Eyes:		May cause severe irritation and lesions.

c.	Ingestion:	May chemically burn mouth and throat, nausea, vomiting, abdominal

pain and diarrhea.  Ferrous Sulphate constituent is moderately toxic,

lethal at 5-113 grams.

d.	Skin:		May burn on extended contact, or on moist or injured skin.

- CHRONIC:	Potassium sulphate aggravates kidney disorders.

- EMERGENCY FIRST AID PROCEDURES

Inhalation – Remove from exposure area.  If irritation exists from mists, or in the event of massive inhalation, seek medical attention.

Eyes – immediately flush eyes with plenty of water for at least 15 minutes.  Seek medical attention.

Ingestion Give as much warm water as possible, seek medical attention immediately.  Never give anything by mouth to an unconscious person.  If symptoms of central nervous stimulation occur or a skin rash is present, give 10% dextrose in water.  The dextrose should be continued at high intake both to induce diuresis and because it has been reported to have a binding effect on circulating boron molecules.

Skin – Wash thoroughly with soap and water.  Rinse thoroughly; seek medical attention if inflammation occurs.  Do not attempt to neutralize with chemicals.

PAGE 2 OF 3

SECTION VII	PERSONAL PROTECTION AND CONTROLS

- Respiratory Protection – As required by conditions.  Use an OSHA or NIOSH approved respirator if required.

- VENTILATION:  General ventilation is usually adequate.  Local exhaust should be used if needed, for safe, comfortable working conditions.

- SKIN AND EYE PROTECTION:  Safety glasses should be worn in any type of operation.

Protective gloves should be worn as good hygiene dictates.

- OTHER CONTROL MEASURES:  An eye bath and washing facilities should be available.

Wash thoroughly after handling.  Do not smoke when handling chemicals.

SECTION VIII                           SPECIAL STORAGE AND HANDLING PRECAUTIONS

Since emptied packages retain product residue, follow label warnings even after package is emptied.

A review of work literature and Eastman Kodak’s observation of their own employees have noted no reports of neurotoxiciity, pulmonary disease, or metal fume fever (associated with Manganese ore mining operations) from exposure to manganese sulfate.

# SECTION IX	ENVIRONMENTAL PROCEDURES

Steps to be taken in case material is released or spilled.  Collect and contain for salvage or disposal.  Absorb waste on inert media and dispose of as solid waste.

Waste Disposal Method:  Landfill in compliance with all federal, state and local laws concerning health and environment.

# SECTION X	ENVIRONMENTAL EFFECTS DATA

SUMMARY:  This product has not been tested for environmental effects.  If discharged into the marine environment it may be toxic to fish or other marine organisms and due to its nutrient value may contribute to eutophication in bodies of water.  The available data on the raw materials does not indicate any undue hazard to the environment under anticipated conditions of storage and use except as noted below:

SECTION XI	TRANSPORTATION

DOT Hazard Classification:	Corrosive liquids, N.O.S. ( Iron Sulphate, Magnesium Chloride

and Zinc Sulphate mixtures), Class 8 (9.2) UN 1760, PG III

Stoller Chemical believes the information contained in this Material Safety Data Sheet is accurate based on the information supplied by reputable suppliers of our raw materials.  The information contained herein is furnished without warranty of any kind.  Users should consider this data only as a supplement to other information gathered by them and must make independent determinations of suitability and completeness of information from all sources to assure proper use and disposal of these materials and the safety and health of employees and customers.

January 2013		PAGE 3 OF 3