MATERIAL SAFETY DATA SHEET

# SECTION I	IDENTIFICATION				Canada

Emergency Phone Number	CHEM-TEL, INC. 1-800-424-9300

Chemical Family	Sulphate

Chemical Name & Synonyms:	N/A – Mixture

Formula:	Proprietary

Trade Name & Synonym:	THIS FLOWABLE 4.4% COPPER & SULFUR

SARA/TITLE III HAZARD CATEGORIES (See Section X)

Immediate (ACUTE) Health:  No                         Reactive Hazard:     No

Delayed (Chronic) Health:      Yes                        Sudden Release

Fire Hazard:                             No                         of Pressure:              No

# SECTION II	PRODUCT AND COMPONENT HAZARD DATA

A.	COMPONENTS	CAS. REG. NO        APPROX %         TLV

Tri-basic Copper Sulphate	1332-14-5                     9%                 TLV-TWM 1 mg/m3 as Cu

Sulphur                                     7704-34-9                    50%                Not established

# SECTION III	PHYSICAL DATA

Appearance and Odor:	Greenish-yellow; viscous liquid, Sulphur odour

Boiling Point:	Not established

Specific Gravity:	1.50

Vapor Pressure:	Not established

Percent Volatile by Volume:	Proprietary

Vapor Density (Air = 1)                          >1.0 (water vapor)

Evaporation Rate:	(Ethyl Ether = 1): <1

Solubility in Water:	Insoluble but miscible

# SECTION IV	FIRE AND EXPLOSION HAZARD DATA

Flash Point:	N/A

Flammable Limits:	LEL:  not set   UEL:  not est.

Extinguishing Agent:	Water, CO2 or Dry Materials

Special Fire Fighting Procedures:	Wear self-contained breathing apparatus

Unusual Fire and Explosion Hazards:	Toxic fumes may be generated at elevated temperatures.

Hazards:

# SECTION V	REACTIVITY DATA

Stability:	Stable

Incompatibility:	Oxidizers

Hazardous Decomposition Products:	SO2  may be evolved above 300 C

Hazardous Polymerization:	Will not occur

Products:

PAGE 1 OF 3

SECTION VI	TOXICITY AND HEALTH

- EXPOSURE LIMITS

OSHA Permissible Exposure Limit (PEL):   Not established

Threshold Limit Value (TLV):	     1 mg Cu/m3

- EFFECTS OF OVEREXPOSURE

- ACUTE

a.	Inhalation:	Irritation

b.	Eyes:		Irritation. Possible cornea injury

c.	Ingestion:	Nausea, gastric distress, vomiting, diarrhea.

Very large quantities may produce convulsions, shock, coma.

d.	Skin:		May cause irritation.

- CHRONIC:                      CNS, liver and kidney damage from prolonged overexposure.

- EMERGENCY FIRST AID PROCEDURES

Inhalation – Remove from exposure area.  If irritation exists from mists, or in the event of massive

inhalation, seek medical attention.

Eyes – Immediately flush eyes with water for 15 minutes, seek medical attention.

Ingestion – Drink large amounts of  water  for at least 15 minutes.  Seek  medical attention.

Skin – Wash with soap and water.  Rinse thoroughly; seek medical attention if inflammation occurs.

Do not attempt to neutralize with chemicals.

- ANIMAL TOXICITY DATA

Copper Sulphate LD50 (oral—rat) 300 mg/kg

Copper Sulphate TDL0 (oral-human) 11 mg/kg

SECTION VII	PERSONAL PROTECTION AND CONTROLS

- Respiratory Protection – As required by conditions.  Use an OSHA or NIOSH approved respirator if required.

- VENTILATION:  General ventilation is usually adequate.  Use if needed for safe, comfortable working conditions.

- SKIN AND EYE PROTECTION:  Safety glasses should be worn in any type of operation.

Protective gloves should be worn as good hygiene dictates.

- OTHER CONTROL MEASURES:  An eye bath and washing facilities should be available.

Wash thoroughly after handling. Do not smoke when handling chemicals.

SECTION VIII	SPECIAL STORAGE AND HANDLING PRECAUTIONS

Since emptied packages retain product residue, follow label warnings even after package is emptied.

PAGE 2 OF 3

SECTION IX	SPILL, LEAK AND DISPOSAL PRACTICES

Steps to be taken in case material is released or spilled.  Collect and contain for salvage or disposal.  Absorb waste on inert media and dispose of as solid waste.

Waste Disposal Method:  Landfill in compliance with all federal, state and local laws concerning health and environment.

SECTION X	ENVIRONMENTAL EFFECTS DATA

To aid our  customers in complying with regulatory requirements, SARA Title III hazard categories for this product are indicated in Section I.  If the word “YES” appears next to any category, this product may be reportable by you under the requirements of 40 CFR Part 370.  Please consult those regulations for details.

SECTION XI                    TRANSPORTATION DOT  HAZARD CLASSIFICATION

DOT Hazard Classification:    COPPER CHLORIDE,, SOLUTION, Class 8 ( 9.2)

UN 2802, P.G. III

Stoller Chemical believes the information contained in this material safety data sheet is accurate based on the information by reputable suppliers of our raw materials.  This information contained herein is furnished without warranty of any  kind.  Users should consider these data only as a supplement to other information gathered by them and must make independent determinations of suitability and completeness of information from all sources to assure proper use and disposal of these materials and safety and health of employees and customers.

January 2013

Page 3 of 3