Safety Data Sheet OSHA Hazard Communication Standard  29 CFR 1910.1200. Prepared to GHS Rev 3.

Revision date:  Initial version Date of issue: 09.30.2015

Page: 1/12

Product name: 36% Zinc Oxy-Sulfate

SECTION 1: Identification

Product identifier used on the label:  Product Name: 36% Zinc Oxy-Sulfate.

Other means of identification: Synonyms: None available Product Code Number: 2ZN360000K00, 2ZN362500B50, 2ZN362200B50,

ZN362000T00, ZN362500T00. SDS number:  CC001US

Recommended use of the chemical and restrictions on use: Recommended use:  Fertilizer Micronutrient Additive. Recommended restrictions:  Not intended for human consumption.

Name, address, and telephone number of the chemical manufacturer, importer, or other

responsible party: Company Name: Cameron Chemicals, Inc. Company Address: 830 Old Dill Road,

Suffolk, VA 23434 Company Telephone: (757) 934-2142 8.00am to 5.00pm

Company Contact Name Mark Whitfield Company Contact Email mwhitfield@cameronchemicals.com

Emergency phone number: Chemtrec USA:  800-424-9300 (24hrs)

SECTION 2: Hazard(s) identification

Classification of the chemical in accordance with paragraph (d) of §1910.1200:

Physical hazards

No physical hazards under GHS.

Health hazards

Skin irritation, Category 2. Serious eye damage, Category 1. Specific target organ toxicity - single exposure, Category 3, Respiratory system.

36% Zinc Oxy-Sulfate

SDS#: CC001US

Environmental hazards

Not adopted under OSHA GHS

GHS Signal word: 	DANGER.

GHS Hazard statement(s): 	H315 - Causes skin irritation H318 - Causes serious eye damage H335 - May cause respiratory irritation

.

GHS Hazard symbol(s):

GHS Precautionary statement(s):

Prevention:

Avoid breathing dust/fume/gas/mist/ vapors/spray.

Wash skin thoroughly after handling.

Use only outdoors or in a well-ventilated area.

Wear protective gloves/protective clothing/eye protection/face protection.

Response:

If on skin: Wash with plenty of water.

If inhaled: Remove person to fresh air and keep comfortable for breathing.

If in eyes: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing.

Immediately call a poison center/doctor.

Specific treatment (see sections 4 to 8 on this SDS and any additional information on this label).

If skin irritation occurs: Get medical advice/attention.

Take off contaminated clothing and wash it before reuse.

Storage:

Store in a well-ventilated place. Keep container tightly closed.

Store locked up.

Disposal:

• Dispose of contents/container to a suitable treatment site in accordance with local/regional/international regulations.

Hazard(s) not otherwise Classified (HNOC): None known.

36% Zinc Oxy-Sulfate

SDS#: CC001US

Percentage of ingredient(s) of unknown acute toxicity:

96% of the mixture consists of ingredients of unknown acute toxicity (oral/dermal/inhalation).

SECTION 3: Composition/information on ingredients

Mixture: Oxides and Sulfates of Zinc.

| Chemical name | CAS# | Concentration (weight %) |
| --- | --- | --- |
| Zinc Oxide | 1314-13-2 | 30 – 50% |
| Zinc Sulfate | 7733-02-0 | 10 - 30% |
| Iron Oxide | 1309-37-1 | 15 – 25% |
| Calcium Oxide | 1305-78-8 | 3 – 5% |

Note: The balance of the ingredients are not classified as hazardous or are below the concentration limit to be classified as hazardous, under the criteria of the Federal OSHA Hazard Communication Standard 29CFR 1910.1200.

SECTION 4: First-aid Measures

Description of necessary measures: Inhalation: Remove victim to fresh air immediately. Give oxygen or artificial respiration as needed. Obtain emergency medical attention. Prompt action is essential.

Skin contact: Wash with plenty of water. Seek medical attention if irritation persists.

Eye contact: Wash the eyes with running water for at least 15 minutes, occasionally lifting the upper and lower eyelids. If irritation persists, seek medical attention.

Ingestion: Rinse mouth and then drink plenty of water. Induce vomiting (lean victim forward to reduce risk of aspiration). Never induce vomiting or give anything by mouth if the victim is unconscious or having convulsions. Obtain emergency medical attention.

Most important symptoms/effects, acute and delayed:

Eye irritation may occur. Prolonged dermal exposure may cause skin irritation.  Ingestion may cause stomach upset. Occasional mild irritation effects to the nose and throat may occur from inhalation.

Indication of immediate medical attention and special treatment needed, if necessary: If any symptoms are observed, contact a physician and give them this SDS sheet. Treat symptomatically.

SECTION 5: Fire-fighting measures

36% Zinc Oxy-Sulfate

SDS#: CC001US

Suitable extinguishing media: Product is not combustible. Use extinguishing media that is suitable for surrounding materials. Unsuitable extinguishing media: None known.

Specific hazards arising from the chemical:

None expected.

Special protective equipment and precautions for fire-fighters: Wear self-contained breathing apparatus and protective clothing. In addition, wear other appropriate protective equipment as conditions warrant (see Section 8).

SECTION 6: Accidental release measures

Personal precautions, protective equipment and emergency procedures:  Ensure adequate ventilation. Evacuate personnel to safe areas. Wear appropriate protective equipment, including respiratory protection, as conditions warrant (see Section 8). See Sections 2 and 7 for additional information on hazards and precautionary measures.

Methods and materials for containment and cleaning up:

Small Spills: Sweep up and try to keep dust to a minimum. Large Spills: Sweep up and try to keep dust to a minimum. Containment: Do not release into sewers or waterways. See Section 13 for information on appropriate disposal.

SECTION 7: Handling and Storage

Precautions for safe handling: Use proper safety equipment at all times. Use good personal hygiene practices and wear appropriate personal protective equipment (see section 8). Wash hands before breaks and at the end of work. Clothing being used around chemicals should be cleaned daily.

Conditions for safe storage, including any incompatibles:

Store materials in a cool dry place away from heat and open flame. Store only in the original container. Keep container tightly closed.

SECTION 8: Exposure controls/personal protection

OSHA permissible exposure limit (PEL), American Conference of Governmental Industrial Hygienists (ACGIH) Threshold Limit Value (TLV), and any other exposure limit used or recommended by the chemical manufacturer, importer, or employer preparing the safety data sheet, where available:

| Zinc Oxide | 5 mg/m3 | None known |
| --- | --- | --- |
| Zinc Sulfate (Zinc compounds) | 5 mg/m3 | None known |
| Iron Oxide | 5 mg/m3 | None known |
| Calcium Oxide | 5 mg/m3 | None known |

| US ACGIH Threshold Limit Values |  |  |
| --- | --- | --- |
| Substance | TLV-TWA | TLV-STEL | REMARKS |
| Zinc Oxide | 2 mg/m3 | 10 mg/m3 | Metal fume fever |
| Zinc Sulfate (Zinc compounds) | 10 mg/m3 | None known | n/a |
| Iron Oxide | 5 mg/m3 | None known | Pneumoconiosis Not classifiable as a human carcinogen |
| Calcium Oxide | 2 mg/m3 | None known | Upper Respiratory Tract irritation |

| US NIOSH NIOSH Recommended Exposure Limits |  |
| --- | --- |
| Substance | TLV-TWA | TLV-STEL |
| Zinc Oxide | 5 mg/m3 | 10 mg/m3 |
| Zinc Sulfate | None known | None known |
| Iron Oxide | 5 mg/m3 | None known |
| Calcium Oxide | 2 mg/m3 | None known |

Appropriate engineering controls: Provide general or local exhaust ventilation systems to maintain airborne concentrations below OSHA PELs. Local exhaust ventilation is preferred because it prevents contaminant dispersion into the work area by controlling it at its source.

Individual protection measures, such as personal protective equipment:

Eye/face protection: Wear protective eyeglasses or chemical safety goggles, per OSHA eye- and face-protection regulations (29 CFR 1910.133). Contact lenses are not eye protective devices. Appropriate eye protection must be worn instead of, or in conjunction with contact lenses.

Skin and Hand protection: Wear protective gloves, boots, and aprons to prevent prolonged or repeated skin contact. Gloves must be inspected prior to use. Use proper glove removal technique (without touching glove's outer surface) to avoid skin contact with this product. Dispose of contaminated gloves after use in accordance with applicable laws and good laboratory practices. Wash and dry hands.

Respiratory protection: Seek professional advice prior to respirator selection and use. Follow OSHA respirator regulations (29 CFR 1910.134) and, if necessary, wear a MSHA/NIOSHapproved respirator. Select respirator based on its suitability to provide adequate worker protection for given working conditions, level of airborne contamination, and presence of sufficient oxygen. If respirators are used, OSHA requires a written respiratory protection program that includes at least: medical certification, training, fit-testing, periodic environmental monitoring, maintenance, inspection, cleaning, and convenient, sanitary storage areas.

Other:

Safety Stations: Make emergency eyewash stations, safety/quick-drench showers, and washing facilities available in work area. Contaminated Equipment: Separate contaminated work clothes from street clothes. Launder before reuse. Remove this material from your shoes and clean personal protective equipment. Comments: Never eat, drink, or smoke in work areas. Practice good personal hygiene after using this material, especially before eating, drinking, smoking, using the toilet, or applying cosmetics. Consider periodic medical exams of exposed workers with emphasis on skin, respiratory, and blood screening.

Thermal hazards: None established.

SECTION 9: Physical and chemical properties

Appearance (physical state, color, etc.): Granular solid Color: Gray. Odor: No odor. Odor threshold: Not established pH: No data available Melting point/freezing point: No data available Initial Boiling Point and  No data available boiling range:   Flash point: No data available Evaporation rate: No data available Flammability (solid, gas): Not flammable Upper/lower flammability or explosive limits

Flammability limit – lower %): No data available     Flammability limit – upper (%): No data available    Explosive limit – lower (%): No data available    Explosive limit – upper (%): No data available

Vapor pressure: No data available Vapor density (air=1): No data available Relative density (water = 1): No data available Solubility(ies): Partially Soluble Partition coefficient  n-octanol/water: No data available

36% Zinc Oxy-Sulfate

SDS#: CC001US

Auto-ignition temperature: No data available Decomposition temperature: Not established Viscosity: No data available Density: 80lbs Cubic Foot

SECTION 10: Stability and Reactivity

Reactivity: Stable. Chemical stability: This product is stable at room temperature in closed

containers under normal storage and handling conditions. Possibility of hazardous reactions: Hazardous polymerization cannot occur. Conditions to avoid: Avoid moisture. Incompatible materials: Strong oxidizing agents. Hazardous decomposition products: None expected.

SECTION 11: Toxicological information

Information on likely routes of exposure:

| Inhalation: | Inhalation is the most significant route of exposure in occupational and other settings. |
| --- | --- |
| Ingestion: | An expected route of entry. Ingestion may cause stomach upset. |
| Skin: | An expected route of entry. Prolonged dermal exposure may cause skin irritation. |
| Eyes: | Not a primary route of entry but may cause irritation. |
| Target Organ(s): | Eyes, Skin, Respiratory system. |

Symptoms related to the physical, chemical, and toxicological characteristics:

Eye irritation may occur. Ingestion may cause stomach upset. Occasional mild irritation effects to the nose and throat may occur from inhalation.

Delayed and immediate effects and chronic effects from short or long-term exposure:

Prolonged dermal exposure may cause skin irritation.

Numerical measures of toxicity:

Acute toxicity estimates: Ingredient Information:

| Substance | Test Type (species) | Value |
| --- | --- | --- |
|  | LD50 Oral (Mouse) | 7950 mg/kg |
| Zinc Oxide | LD50 Dermal (Rat) | No known data |
|  | LC50 Inhalation (Mouse) | 2500 mg/m3 |

| Zinc Sulfate | LD50 Oral (Rat) | No known data |
| --- | --- | --- |
|  | LD50 Dermal (Rat) | No known data |
|  | LC50 Inhalation (Rat) | No known data |
|  | LD50 Oral (Rat) | No known data |
| Iron Oxide | LD50 Dermal (Rat) | No known data |
|  | LC50 Inhalation (Rat) | No known data |
|  | LD50 Oral (Rat) | No known data |
| Calcium Oxide | LD50 Dermal (Rat) | No known data |
|  | LC50 Inhalation (Rat) | No known data |

| Skin corrosion/irritation: | Prolonged dermal exposure may cause skin irritation. |
| --- | --- |
| Serious eye damage/eye irritation: | May cause eye irritation. |
| Respiratory sensitization: | No information available on the mixture, however none of |
|  | the components have been classified as a respiratory |
|  | sensitizer (or are below the concentration threshold for |
|  | classification). |
| Skin sensitization: | No information available on the mixture, however none of |
|  | the components have been classified as a skin sensitizer (or |
|  | are below the concentration threshold for classification). |
| Germ cell mutagenicity: | No information available on the mixture, however none of |
|  | the components have been classified as causing germ cell |
|  | mutagenicity (or are below the concentration threshold for |
|  | classification). |
| Carcinogenicity: | No information available on the mixture, however none of |
|  | the components are listed in the National Toxicology |
|  | Program (NTP) Report on Carcinogens (latest edition) or has |
|  | been found to be a potential carcinogen in the International |
|  | Agency for Research on Cancer (IARC) Monographs (latest |
|  | edition), or by OSHA. |
| Reproductive toxicity: | No information available on the mixture, however none of |
|  | the components have been classified as causing reproductive |
|  | toxicity (or are below the concentration threshold for |
|  | classification). |
| Specific target organ toxicity- |  |
| Single exposure: | No information available on the mixture, however Iron oxide |
|  | and Calcium oxide are known to cause respiratory irritation. |
| Specific target organ toxicity- |  |
| Revision Date: Sept 30, 2015 | Page 8 of 12 |

36% Zinc Oxy-Sulfate

SDS#: CC001US

Repeat exposure: No information available on the mixture, however none of the components have been classified as causing Specific target organ toxicity, repeat exposure (or are below the concentration threshold for classification).

Aspiration hazard: No information available on the mixture, however none of the components have been classified as causing an aspiration (or are below the concentration threshold for classification).

SECTION 12: Ecological information

Ecotoxicity (aquatic and terrestrial, where available): Ingredient Information:

| Substance | Test Type | Species | Value |
| --- | --- | --- | --- |
| Zinc Oxide | LC50 | Fish - Oncorhynchus mykiss (rainbow trout) | 1.1 mg/l – 96h |
|  | EC50 | Invertebrate - Daphnia magna (Water flea) | 0.098 mg/l – 48h |
|  | EC50 | Algae | No data available |
| Zinc Sulfate | LC50 | Fish | No data available |
|  | EC50 | Invertebrate | No data available |
|  | EC50 | Algae | No data available |
| Iron Oxide | LC50 | Fish | No data available |
|  | EC50 | Invertebrate | No data available |
|  | EC50 | Algae | No data available |
| Calcium Oxide | LC50 | Fish - Cyprinus carpio (Carp) | 1070 mg/l - 96 h |
|  | EC50 | Invertebrate | No data available |
|  | EC50 | Algae | No data available |

| Persistence and Degradability: | Not determined |
| --- | --- |
| Bioaccumulative Potential: | This material is not expected to bioaccumulate. |
| Mobility in Soil: | On soil this product may leach into the groundwater. |
|  | Because it is slightly soluble, removal by rain, snow or other |
|  | precipitation is possible |
| Other adverse effects (such as |  |
| hazardous to the ozone layer): | No additional information available. |

SECTION 13: Disposal considerations

Description of waste residues and information on their safe handling and methods of disposal,  including the disposal of any contaminated packaging:

Product - Contact your supplier or a licensed contractor for detailed recommendations. Follow  applicable Federal, state, and local regulations.  This product has been evaluated for RCRA  characteristics and should not meet the criteria of a hazardous waste if discarded in its purchased  form.  Under RCRA, it is the responsibility of the user of the product to determine at the time of  disposal, whether the product meets RCRA criteria for hazardous waste.  This is because product uses, transformations, mixtures, processes, etc., may render the resulting materials hazardous. . Contaminated packaging - Contaminated packaging may contain residues of product. Dispose of in  the same manner as product. Comply with applicable local, state or international regulations  concerning solid or hazardous waste disposal and/or container disposal.

SECTION 14: Transport Information

Land transport DOT

UN number  UN 3077 UN proper shipping name Environmentally hazardous substance, solid, N.O.S. (Zinc oxide,

Zinc sulphate) Transport hazard class(es) 9 Packing group, if necessary  III

Maritime transport IMDG

UN number  UN 3077 UN proper shipping name Environmentally hazardous substance, solid, N.O.S. (Zinc oxide,

Zinc sulphate) Transport hazard class(es) 9 Packing group, if necessary  III

Air transport ICAO-TI and IATA-DGR

UN number  UN 3077 UN proper shipping name Environmentally hazardous substance, solid, N.O.S. (Zinc oxide,

Zinc sulphate) Transport hazard class(es) 9 Packing group, if necessary  III

Environmental hazards

Marine pollutant: Yes.

Transport in bulk (according to Annex II of MARPOL 73/78 and the IBC Code)

No further relevant information available.

36% Zinc Oxy-Sulfate

SDS#: CC001US

Special precautions which a user needs to be aware of, or needs to comply with, in connection with transport or conveyance either within or outside their premises.

None.

SECTION  15: Regulatory Information

Safety, health and environmental regulations specific for the product in question.

USA: United States Federal Regulations: This SDS complies with the OSHA, 29 CFR 1910.1200. This product is hazardous under OSHA.

Toxic Substances Control Act (TSCA) – This substance is listed, as required, on the TSCA

inventory.

SARA Title III

Section 302 Extremely Hazardous Substance (40 CFR 355, Appendix A): None

Section 311/312 (40 CFR 370): Acute Health Hazard: Yes Chronic Health Hazard: No Fire Hazard: No Pressure Hazard: No Reactivity Hazard: No

Section 313 Toxic Release Inventory (40 CFR 372): Zinc oxide and Zinc Sulfate are listed.

STATE REGULATIONS:

This SD’S contains specific health and safety data is applicable for state requirements. For details on your regulatory requirements you should contact the appropriate agency in your state.

California Proposition 65 (California Safe Drinking Water and Toxic Enforcement Act of 1986:

This product does not contain any chemicals known to State of California to cause cancer, birth defects, or any other reproductive harm.

Massachusetts Right to Know: Zinc oxide, Zinc Sulfate, Iron Oxide (as Diiron trioxide) and Calcium oxide are listed on the Massachusetts Right to Know List.

New Jersey Right to Know: Zinc oxide, Zinc Sulfate, Iron Oxide (as Diiron trioxide) and

Calcium oxide are listed on the New Jersey Right to Know list.

Pennsylvania Right to Know: Zinc oxide, Zinc Sulfate, Iron Oxide (as Diiron trioxide) and

Calcium oxide are listed on the Pennsylvania Right to Know List.

SECTION 16: Other information, including date of preparation or last revision

Revision Date: Sept 30, 2015

NFPA Rating

Health hazard: 1 Fire Hazard: 0  Reactivity Hazard: 0

This document is generated for the purpose of distributing health, safety, and environmental data. Information is correct to the best of our knowledge at the date of SDS publication. It is not a specification sheet nor should any displayed data be construed as a specification. The information on this SDS was obtained from sources which we believe are reliable.  However, the information is provided without any warranty, expressed or implied, regarding its correctness. Some information presented and conclusions drawn herein are from sources other than direct test data on the substance itself. The conditions or methods of handling, storage, use and disposal of the product are beyond our control and may be beyond our knowledge.  For this and other reasons, WE DO NOT ASSUME RESPONSIBILITY AND EXPRESSLY DISCLAIM LIABILITY FOR LOSS, DAMAGE, OR EXPENSE ARISING OUT OF OR IN ANY WAY CONNECTED WITH HANDLING, STORAGE, USE, OR DISPOSAL OF THIS PRODUCT. If the product is used as a component in another product, this SDS information may not be applicable.